## Slide 1: Investigating Effects of Nonlinear Acoustic Propagation on Shear Wave Speed Estimates
Ningrui Li
Lab Meeting, April 24, 2015

## Slide 2: Objectives
Determine if varying the degree of nonlinearity in acoustic propagation causes changes in shear wave speed estimates at different focal depths.

## Slide 3: Methods
Generate intensity fields using 3D KZK simulation with various attenuation and nonlinearity coefficients.
Simulate stresses and corresponding axial displacements using LS-DYNA and FEM post-processing tools.

## Slide 4: Methods – Generating Intensity Fields
Simulated C5-2 using Field II
  2.36 MHz, 7 cycles, amplitude
  30 mm and 70 mm focal depths
α = [0.005, 0.3, 0.45, 1.0, 1.5] dB/cm/MHz
β = [0.0, 3.5, 7.0]

## Slide 5: Validation with Field II – 30 mm Focus
Axial intensities down the center (lat = 0mm, ele = 0mm)
α = 0.005 dB/cm/MHz
β = 0
Notes: Next series of plots are all center trace plots -> plots of axial intensities down the center of mesh.

## Slide 6: Validation with Field II – 70 mm Focus
α = 0.45 dB/cm/MHz
α = 0 dB/cm/MHz
Notes: Attenuation differences between Field II and KZK sim? Match up slightly better for no attenuation cases for identical sim inputs when KZK sim run in linear mode.

## Slide 7: Intensity Fields with Increasing Nonlinearity
Notes: As nonlinearity increases, the peak intensities occur at shallower depths. However, nonlinear affects are mitigated for greater attenuation levels.

## Slide 8: Intensity Fields with Increasing Nonlinearity
β = 3.5
β = 0.0
β = 7.0
70 mm focus, α = 0.005 dB/cm/MHz
depth
lateral

## Slide 9: Intensity Fields with Increasing Nonlinearity
β = 3.5
β = 0.0
β = 7.0
70 mm focus, α = 1.0 dB/cm/MHz
depth
lateral

## Slide 10: Intensity Fields with Increasing Nonlinearity
β = 3.5
depth
elevation
β = 0.0
-
=
Notes: Possible out-of-plane sources???

## Slide 11: Methods – Shear Wave Simulations
Imitated dyna*.mat intensity output file
    Linearly interpolated 3D KZK sim intensity output to uniformly spaced set of nodes
    Exploited quarter symmetry → added boundary conditions and PMLs
Simulated ARFI excitation in LS-DYNA
  E = 3.0 kPa, ν = 0.45 (quick runtimes)
  300 μs excitation duration, 25 ms total duration

## Slide 12: Axial Displacements Plot

## Slide 13: Time-to-Peak Shear Wave Speed Estimation

## Slide 14: Expected SWS Calculation

## Slide 15: SWS Measurements at Different Focal Depths