## Slide 1
Simulating the Effects of Nonlinear Acoustic Propagation on Radiation Force
Ningrui Li, Mark L. Palmeri, Kathryn R. Nightingale
Department of Biomedical Engineering, Duke University, Durham, NC, United States.
RESULTS
INTRODUCTION
CONCLUSIONS
REFERENCES
METHODS
RESULTS
Shear waves can be induced in tissues by acoustic radiation force created using an ultrasound probe. The shear wave speed of tissue can be measured by tracking the propagation of shear waves from their source using time-of-flight methods [1]. Tissue stiffness can be characterized using these shear wave speed measurements.
Shear wave speed measurements have been shown to exhibit a depth dependent bias, which has the potential to cause misdiagnosis [2]. It was hypothesized that this depth dependence was caused by out-of-plane shear wave sources generated through nonlinear effects in acoustic propagation. These nonlinear effects are due to localized heating caused by acoustic waves with high pressure amplitudes This increases the sound speed in that specific region. Figure 1 shows the resulting sawtooth wave.
The Khokhlov-Zabolotskaya-Kuznetsov (KZK) nonlinear wave equation [3] was used to simulate acoustic waves propagating in differing media with various nonlinear coefficients. The simulated intensity field distributions showed that as nonlinearity increased, the maximum intensities tended towards shallower, laterally offset locations. It was also shown that as attenuation increased, the effects of nonlinearity were also diminished.
[1] Sarvazyan, A. P., Rudenko, O. V., Swanson, S. D., Fowlkes, J. B., & Emelianov, S. Y. (1998). Shear wave elasticity imaging: a new ultrasonic technology of medical diagnostics. Ultrasound in medicine & biology, 24(9), 1419-1435.
[2] Zhao, H., Song, P., Urban, M. W., Kinnick, R. R., Yin, M., Greenleaf, J. F., & Chen, S. (2011). Bias observed in time-of-flight shear wave speed measurements using radiation force of a focused ultrasound beam. Ultrasound in medicine & biology, 37(11), 1884-1892.
[3] Pinton, G. F., Dahl, J., Rosenzweig, S., & Trahey, G. E. (2009). A heterogeneous nonlinear attenuating full-wave model of ultrasound. Ultrasonics, Ferroelectrics, and Frequency Control, IEEE Transactions on, 56(3), 474-488.
α = 0.005 dB/cm/MHz
α = 1.5 dB/cm/MHz
The
A curvilinear C5-2 transducer focused at 70 mm in depth was simulated with 7 excitation cycles at an excitation frequency of 2.36 MHz to generate the face pressures used as an input to the KZK simulations. These face pressure waves was scaled to an amplitude of 0.4 MPa to match pressure amplitudes that were measured experimentally. As shown in Figure 2, appropriate time delays were applied to focus the acoustic waves correctly.
Figure 1: Nonlinear Acoustic Wave
Using these face pressure inputs, KZK simulations were run with various combinations of attenuation coefficients (α = 0.005, 0.3, 1.0, and 1.5 dB/cm/MHz) and nonlinear coefficients (β = 0, 3.5, and 7). The resulting intensity fields were visualized using ParaView.
Figure 2: Simulated Element Time Delays
β = 0
β = 3.5
β = 7
β = 0
β = 3.5
β = 7
Notes: 1